1. Consider the computation (m1+m2)+(m3*m4) where m1, . . . denote the content of
memory locations.

(a) Write assembly code typical of RISC machines for this computation. Use at most two operands for each instruction (e.g., ADD r1 r2 for r1 <- r1 + r2) and use at most three registers altogether. The result of the computation should be stored in a register.

I1:	LOAD r1, m1
I2:	LOAD r2, m2
I3:	ADD r1, r2
I4:	LOAD r2, m3
I5:	LOAD r3, m4
I6:	ADD r2, r3
I7:	MUL r1, r2

(b) Briefly describe the main idea for superscalar processors.

A superscalar CPU is CPU that can process more than one instruction per cycle in parallel. For example if CPU has several ALU unit it can execute several arithmetic operations at once. It is often combined with pipelining, which allows CPU to concurrently have different stages of instruction cycles, and out-of-order, which allows CPU to .

(c) Show the pipeline activity by drawing a diagram when the assembly code is executed on a superscalar processor. There are four pipeline stages: fetch– decode, register-read, execute and write-back, and there are two functional units for each pipeline stage. State you additional assumptions.

Cycle	Fetch-Decode	Register Read	Execute	Write Back
1	I1, I2
2	I3, I4		I1, I2
3	I5, I6			I1, I2
4	I7	I3	I4, I5
5			I3	I4, I5
6		I6		I3
7			I6
8				I6
9		I7
10			I7
11				I7

2. (a) List the most important registers in a generic CPU and briefly explain their
functions.

Program counter – hold info about next instruction
Instruction Register – current instruction
Memory Buffer Register – data from memory
Memory Address Register – address in memory
Program status word – CPU status
Accumulator – results of ALU
General registers – temporary data

(b) Briefly describe the compiler-based register optimization technique (typically
used for RISC machines).

Compiler based register optimization technique

(c) Explain what register windows are and how they are used to improve performance.

These are registers that hold instruction after fetch-decode phase.
3. Consider the following attempt to solve the critical section problem for two processes where the initial value of turn is 0 or 1:

P0
while(TRUE){
while(turn!=0);
critical-section();
turn=1;
noncritical-section();
}

P1
while(TRUE){
while(turn!=1);
critical-section();
turn=0;
noncritical-section();
}

a) Briefly explain the concepts of race condition, critical section and mutual exclusion.

Race condition – when multiple processess/threads wants to access the same resources the results depends which of them will be dispatched first

Critical section – part of the program where share memory is accessed

Mutual exclusion – no two processes can be in critical section at the same time

(b) Explain whether the above code avoids deadlock

Yes, it avoids deadlock because only one program can be in critical section. When turn is set to a given integer it will allow only one program to execute its code and the other process must wait.

(c) Explain whether the above code is starvation free.

It is starvation free because after executing its critical section it change flag to opposite – ie. it blocks this process from re-entering into critical section again. So in the effect processes run one after each other.

4. (a) Explain the benefits of the virtual memory technique.

(b) Explain the concept of locality of reference.

(c) Consider a (RISC) machine that uses 4KB pages and 4-byte instructions, and assume that a process switch just occurred. Loading a page from the hard disk into memory takes 10 ms. The initial probability (after the process switch) that a referenced instruction is in main memory is 0.1. How many milliseconds does it take to load the first referenced instruction into the IR on average? (You can ignore the loading time from main memory into the IR.)

(d) Explain how the situation changes for loading the second instruction, and give an estimate for the average load time in milliseconds for this case. (You can assume that the first instruction referenced is not a jump.)