1. a) Identify the various addressing modes in the assembly code below and explain,
with the use of a mathematical formula, what the program computes.
I1: LOAD r2, M1	r2 ← M1
I2: DIV r1, r2	r1 ← r1/r2
I3: LOAD r2, M2	r2 ← M2
I4: LOAD r3, [r3]	r3 ← [r3]
I5: MUL r2, r3	r2 ← r2 * r3
I6: ADD r1, r2	r1 ← r1 + r2
I7: LOAD r2, M3	r2 ← M3
I8: LOAD r3, M4	r3 ← M4
I9: ADD r2, r3	r2 ← r2 + r3
I10: MUL r1, r2	r1 ← r1 * r2

Immediate:	none
Direct:	I1, I3, I7, I8
Indirect:	none
Register:	I2, I5, I6, I9, I10 (however all instruction address registers)
Register Indirect:	I4

formula = ({r1} over {M1}) + (M2*[r3]) * (M3+M4)

b) Find appropriate words/expressions to replace the numbers [n] so that the text below describes what happens during the indirect cycle. For instance, the first replacement should be [1]=MAR. Note that different numbers may correspond to the same word/expression.

The following text describes the indirect cycle: When indirect (memory) addressing is used in an instruction, the memory reference is put into the [MAR] so that it can be sent to the [MM] via the [address] lines of the bus. At the same time the [CPU] sends a read signal to the [MM] via the [control] lines of the bus. Then the [MM] sends the effective [address] to the [MBR] of the [CPU] via the [data] lines of the bus. If the effective [address] is in the [MM], then another cycle is needed to load the operand.

2. Consider the assembly code from Question 1.
(a) Rewrite the code by using the register renaming technique and explain how this removes false dependencies.

I1: LOAD r2a, M1
I2: DIV r1, r2a
I3: LOAD r2b, M2
I4: LOAD r3a, [r3]
I5: MUL r2b, r3a
I6: ADD r1, r2b
I7: LOAD r2c, M3
I8: LOAD r3b, M4
I9: ADD r2c, r3b
I10: MUL r1, r2c

I have renamed the following registers:
- r2 into r2a, r2b and r2c
- r3 into r3a and r3b
I2 uses r2 jest before this register is going to load M2. By renaming it I3 does not need to wait for I2 to complete – by renaming the registers we eliminate the possibility that I3 would be executed before I2 and thus DIV operation would be wrong. Similar when we doing arithmetic operations (I5 and I6) we can be assured that loading new operand in I7 will not make any problems. Renaming r3 in I5 helps to separete this operation from load instruction I8, followed by add instruction containing new data.

b) Show the execution of your code from Question 2(a) on a five-stage (Fetch, Decode, Register read, Execute, Write back) superscalar processor where there are two functional units for each stage. Assume that instructions are fetched from an onboard instruction cache and that there is an instruction window where all the fetched and decoded instructions can be stored. Use out-of-order execution where possible. Explain when instructions can skip pipeline stages and why delay slots occur.

Cycle	Fetch	Decode	Instruction Window	Register Read	Execute	Write Back
1	I1, I2
2	I3, I4	I1, I2
3	I5, I6	I3, I4	I2 (r2)		I1
4	I7, I8	I5, I6	I2 (r2) / I3 (r2)		I4	I1
5	I9, I10	I7, I8	I3 (r2) / I5 (r2 r3) / I6 (r1 r2) / I7(r2) / I8 (r3)	I2		I4
6		I9, I10	I5 (r2 r3) / I6 (r1 r2) / I7(r2) / I8 (r3)		I2, I3
7			I5 (r2 r3) / I6 (r1 r2) / I7(r2) / I8 (r3) / I9 (r2 r3) / I10 (r2 r1)			I2, I3
8			I6 (r2) / I7(r2) / I8 (r3) / I9 (r2 r3) / I10 (r2 r1)	I5
9			I6 (r2) / I7(r2) / I9 (r2 r3) / I10 (r2 r1)		I5, I8
10			I6 (r2) / I7(r2) / I9 (r2) / I10 (r2 r1)			I5, I8
11			I7(r2) / I9 (r2) / I10 (r2 r1)	I6
12			I9 (r2) / I10 (r2 r1)		I6, I7
13			I9 (r2) / I10 (r2 r1)			I6, I7
14			I10 (r2)	I9
15			I10 (r2)		I9
16			I10 (r2)			I9
17				I10
18					I10
19						I10

Load instruction [Memory → Register] can skip register reading step. Some other examples are: using immediate addresing we can skip Register Read and Execution, loading a content of register skips execution.
Delay slot slot occurs because resource is already used by another instructio.

3. Consider the following code for two processes, P 0 and P 1 (identified by i = 0 and i = 1, respectively). The labels Lk are not part of the code, they are used to identify the lines of the code. The input variables y 0 and y 1 have initial value 0.
L1 : while(true){
L2 : noncritical;
L3 : y i = 1;
L4 : while(y 1−i == 1);
L5 : critical;
L6 : y i = 0;
L7 : }

(a) Determine whether the following general statements about concurrency are true or false.
i. Every deadlock-free code is starvation free.
FALSE
ii. Every starvation-free code is deadlock free.
TRUE
Iii. Every code that ensures the condition progress is starvation free.
FALSE
iv. Every starvation-free code satisfies the condition progress.
TRUE

(b) Determine whether the following statements about the code above are true or false.
i. The code is starvation free.
FALSE
ii. The code achieves mutual exclusion.
TRUE
Iii. At least one of the processes is able to enter its critical section.
TRUE
iv. The code satisfies the condition progress.
TRUE
v. Swapping lines L3 and L4 in the code above would yield a starvation-free
code.
vi. Swapping lines L3 and L4 in the code above would yield a code that satisfies
mutual exclusion.

4. (a) Determine how much CPU time is needed to print a 1 KB document using.

The initial set-up takes 20 milliseconds in each case. It takes 50 microseconds to put a character in the data register of the controller of the printer, and printing one character takes 50 milliseconds. Assume that each interrupt service procedure needed runs for 70 microseconds and that the data register of the controller of the printer can contain only one character.

i. programmed I/O
20 ms
ii. interrupt-driven I/O
20 ms
iii. DMA.
20 ms

(b) A hard disk spins at 6000 rpm (revolutions per minute), and it takes 100 μs (on average) for the head to traverse one track. Consider the following sequence of disk track requests: 27, 129, 110, 186, 147, 41, 10, 64, 120. Assume that initially the head is at track 30 and is moving in the direction of decreasing track numbers. Compute the time it takes to serve the requests using

i. FIFO
ii. SSF (shortest seek first)
iii. SCAN (elevator)
5. (a) Replace the numbers [n] in the text below by appropriate words/expressions so that the text describes addressing when paging is used.

The following text describes addressing when paging is used: Paging uses [virtual] addresses consisting of a [page] number and an [offset], and the system has to translate it to a [physical] address consisting of a [page frame] number and the same [offset]. When a page is referenced first the [TLB], i.e., the [Translation Lookup Buffer] of the [CPU], is checked to see if it includes the corresponding [page table] entry. In case of a hit, the corresponding [frame] number is found and the [physical] address is generated. In case of a miss, the [page table] is accessed. If the referenced page is in [MM], then the [physical] address is generated and the [TLB] is updated. If the referenced page is not in [MM], then the [page] has to be loaded from [Disk], and the [physical] address is generated. Both the [TLB] and the [page tables] are updated.

(b) Find the (unique) correct definition of each of the following concepts
• multiprogramming	VII
• multithreading	IV
• multiprocessing	V

i. The processor can execute several threads at the same time.	PARALLEL PROCESSING
ii. Instructions belonging to several threads can enter the pipeline.
Iii. The execution of threads can be interleaved.
iv. A process is divided into several concurrent paths of execution. MULTITHREADING
v. Several programs can be executed at the same time.	MULTIPROCESSING
vi. Instructions belonging to several programs can enter the pipeline.
Vii. Several processes are executed in an interleaved way.	MULTIPROGRAMMING

(c) Fill in the missing words/expressions to make the following sentences true.

i. Superscalar processors can execute several [instructions] at the same time.
ii. Pipelined processors can overlap various stages of the [instruction cycle].
iii. Threads belonging to the same process share all the [resources] of the process.